## Slide 1: STM8S Training

## Slide 2: Agenda
STM8 Basics & Portifolio
Available Peripherals
Getting Started with the Software and Firmware
  Compiler and IDE
  Library
Tec. Characteristics
Hands-On

## Slide 3: STM8S Training
STM8 Basics & Portifolio

## Slide 4: Internal block Diagram

## Slide 5: Highlights
24MHz Fcpu
2.95 to 5.5V
-40 a +125°C
10K cycles under Flash and 300K under E2PROM
4kBytes to 128kBytes, 20 up to 80 pins
5 different Low Power Modes
IrDA
SWIM programming interface

## Slide 6: STM8S Training
Getting Started

## Slide 7: Where can I find the library and SW?
The library is available here
The STVD (our IDE!) is available here
The compiler is a 3rd part and has no limitation and it’s free!!
http://cosmicsoftware.com/download_stm8_free.php
STSW-STM8069 | STM8S/A Standard peripheral library
STVD | ST Visual develop IDE for developing ST7 and STM8 applications

## Slide 8: Library’s Supported Features

## Slide 9: File Structure

## Slide 10: Library’s Help/User Manual

## Slide 11: Conventions 1/3 

## Slide 12: Conventions 2/3 
The library uses the following naming patern:
  PPP refers to any peripheral acronym, for example TIM2 and TIM3
  System and source/header file names are preceded by the prefix ‘stm8s_’.
  Names of peripheral functions are preceded by the corresponding peripheral acronym in upper case followed by an underscore, for example SPI_SendData.
  Functions used to initialize the PPP peripheral according to parameters specified in the header file are named PPP_Init, for example TIM2_Init
  Functions used to reset the PPP peripheral registers to their default values are named PPP_DeInit, for example TIM2_DeInit
  Functions used to enable or disable the specified PPP peripheral are named PPP_Cmd, for example SPI_Cmd
  Functions used to enable or disable an interrupt source of the specified PPP peripheral are named PPP_ITConfig, for example SPI_ITConfig
  Functions used to check whether the specified PPP flag is set or reset are named PPP_GetFlagStatus, for example I2C_GetFlagStatus
  Functions used to clear a PPP flag are named PPP_ClearFlag, for example I2C_ClearFlag
  Functions used to check whether the specified PPP interrupt has occurred or not are named PPP_GetITStatus, for example TIM2_GetITStatus
  Functions used to clear a PPP interrupt pending bit are named PPP_ClearITPendingBit, for example TIM2_ClearITPendingBit

## Slide 13: Conventions 3/3 
Variable types:
#define __I volatile const /*!< defines 'read only' permissions */
#define __O volatile /*!< defines 'write only' permissions */
#define __IO volatile /*!< defines 'read / write' permissions */
/*!< Signed integer types */
typedef signed char int8_t;
typedef signed short int16_t;
typedef signed long int32_t;
/*!< Unsigned integer types */
typedef unsigned char uint8_t;
typedef unsigned short uint16_t;
typedef unsigned long uint32_t;
/*!< STM8 Standard Peripheral Library old types (maintained for legacy purpose) */
typedef int32_t s32;
typedef int16_t s16;
typedef int8_t s8;
typedef uint32_t u32;
typedef uint16_t u16;
typedef uint8_t u8;
typedef enum {FALSE = 0, TRUE = !FALSE} bool;
typedef enum {RESET = 0, SET = !RESET} FlagStatus, ITStatus, BitStatus, BitAction;
typedef enum {DISABLE = 0, ENABLE = !DISABLE} FunctionalState;

## Slide 14: How to find the available functions

## Slide 15: How to get more info?

## Slide 16: How to get more info?

## Slide 17: How to know the available defines?

## Slide 18: How to know the available defines?

## Slide 19: Library’s Architecture

## Slide 20: Library’s Architecture in files

## Slide 21: Getting Started from scratch!

## Slide 22: Open the STVD

## Slide 23: Choose to create a New Workspace
          And then, to create workspace and project

## Slide 24: Name the workspace and set it’s location

## Slide 25: Select the proper Toolchain

## Slide 26: Select the STM8S003K3

## Slide 27: Your workspace should look like this

## Slide 28: Giving a closer look

## Slide 29: Now, let’s add the library

## Slide 30: Now, let’s add the library

## Slide 31: Now, let’s add the library

## Slide 32: Now, let’s add the library
Once the basic files are imported, we need to add the files responsibles to manage the interrupt vector
  Copy the 3 highlighted files to our project folder, these files are available under the unzip library folder: STM8S_StdPeriph_Lib\Project\STM8S_StdPeriph_Template

## Slide 33: Now, let’s add the library
Since the interrupt vector file that is automatically generated is not asserted with the library’s names, we need to replace the file
  Copy the highlighted file to our project folder, this file is available under the unzip library folder: STM8S_StdPeriph_Lib\Project\STM8S_StdPeriph_Template\STVD\Cosmic

## Slide 34: Now, let’s add the library
With all the preparations done, we just need to add the following files within our project:
  stm8s_it.c
  stm8s_it.h
  stm8s_conf.h
The final result should be like this:

## Slide 35: Configuring the library – stm8s.h

## Slide 36: Configuring the library – stm8s_conf.h
The Standard Peripherals Library implements run-time failure detection by checking the input values of all library functions. The run-time checking is achieved by using an assert_param macro. This macro is used in all library functions which have at least an input parameter. It allows the user to check that the input value lies within the defined parameter values
For the purpouse of this training, we won’t use this feature, so it’s mandatory to comment the assert define:

## Slide 37: Compile the project (F7 as short key)
Once all is done, just compile and get the so desired 0 erros and 0 warnings

## Slide 38: STM8S Training
Tec. Char.

## Slide 39: Programming interface - General Info
SWIM (Single Wire Interface Module):
Direct access to all memory content and RAM
The overall information is transmitted at a 145bytes/ms rate
We do have a simple Stand Alone programmer based on the STM8S discovery kit

## Slide 40: Interrupt – General Info
3 software priorities
32 interrupt vectors already with hardware priorities
Trap and reset interrupts
27 external interrupts, distributed in 6 different vectors

## Slide 41: Flash and EEPROM for the 003
This micro has 8Kb of flash
128B de EEPROM
It doesn’t have the feature Read while Write. Any micro with 16KB or more has this this feature

## Slide 42: Clock
Startup clock: After the reset, the system clock is automatically set to the minimum: 2MHz (HSI/8)
CSS: this feature can be enabled to verify any issues under the HSE and automatically change back to HSI, avoiding any unexpected stop

## Slide 43: STM8S Training
Hands-On

## Slide 44: Hands On
GPIO
ADC
TIM4
UART

## Slide 45: Hands On
GPIO
ADC
TIM4
UART

## Slide 46: Library

## Slide 47: Library

## Slide 48: Library

## Slide 49: Library

## Slide 50: Library

## Slide 51: Library

## Slide 52: GPIO
Turn on and off a simple LED
#include "stm8s.h"
void Delay(u16 nCount)
{
/* Decrement nCount value */
while (nCount != 0)
{
nCount--;
}
}
main()
{
GPIO_Init(GPIOD,GPIO_PIN_0,GPIO_MODE_OUT_PP_HIGH_SLOW);
while (1)
{
GPIO_WriteLow(GPIOD,GPIO_PIN_0);
Delay(9000);
GPIO_WriteHigh(GPIOD,GPIO_PIN_0);
Delay(9000);
}
}

## Slide 53: GPIO
Blink a simple LED, depending on the key status
#include "stm8s.h"
void Delay(u16 nCount)
{
/* Decrement nCount value */
while (nCount != 0)
{
nCount--;
}
}
main()
{
GPIO_Init(GPIOD,GPIO_PIN_0,GPIO_MODE_OUT_PP_HIGH_SLOW);
GPIO_Init(GPIOB,GPIO_PIN_7,GPIO_MODE_IN_PU_NO_IT);
while (1)
{
if(GPIO_ReadInputPin(GPIOB,GPIO_PIN_7) == RESET)
{
GPIO_WriteLow(GPIOD,GPIO_PIN_0);
}
else
{
GPIO_WriteHigh(GPIOD,GPIO_PIN_0);
}
Delay(9000);
}
}

## Slide 54: GPIO
Blink a simple LED, depending on the key status, using external interrupt
  To accomplish this task, we’ll need to add the stm8s_exti.c/h in the project
  main.c
  stm8s_it.c
#include "stm8s.h"
main()
{
GPIO_Init(GPIOD,GPIO_PIN_0,GPIO_MODE_OUT_PP_HIGH_SLOW);
GPIO_Init(GPIOB,GPIO_PIN_7,GPIO_MODE_IN_PU_IT);
EXTI_SetExtIntSensitivity(EXTI_PORT_GPIOB,EXTI_SENSITIVITY_FALL_ONLY);
enableInterrupts();
while (1)
{
}
}
INTERRUPT_HANDLER(EXTI_PORTB_IRQHandler, 4)
{
/* In order to detect unexpected events during development,
it is recommended to set a breakpoint on the following instruction.
*/
GPIO_WriteReverse(GPIOD,GPIO_PIN_0);
}

## Slide 55: Hands On
GPIO
ADC
TIM4
UART

## Slide 56: Library

## Slide 57: Library

## Slide 58: Library

## Slide 59: Library

## Slide 60: Library

## Slide 61: Library

## Slide 62: Library

## Slide 63: ADC
Let’s monitor the ADC value!
  To accomplish this task, we’ll need to add the stm8s_adc1.c/h in the project
  main.c
  To monitor de ADC_Value variable, select it under debug and use the quick watch feature, once enable, right-click in the green area and change it to Read/Write On Fly, the screen selection will turn yellow
#include "stm8s.h"
u16 ADC_Value;
main()
{
GPIO_Init(GPIOB,GPIO_PIN_0,GPIO_MODE_IN_FL_NO_IT );
ADC1_Init(ADC1_CONVERSIONMODE_CONTINUOUS,ADC1_CHANNEL_0,ADC1_PRESSEL_FCPU_D2,
ADC1_EXTTRIG_TIM,DISABLE,ADC1_ALIGN_RIGHT,ADC1_SCHMITTTRIG_CHANNEL0,DISABLE);
ADC1_Cmd(ENABLE);
ADC1_StartConversion();
while (1)
{
if(ADC1_GetFlagStatus(ADC1_FLAG_EOC))
{
ADC_Value = ADC1_GetConversionValue();
}
}
}

## Slide 64: Hands On
GPIO
ADC
TIM4
UART

## Slide 65: Diagrama em bloco

## Slide 66: Library

## Slide 67: Library

## Slide 68: Library

## Slide 69: Library

## Slide 70: Library

## Slide 71: Library

## Slide 72: TIM4
Let’s configure the TIM4 to have a 1KHz frequency and blink our LED every second, using interrupt!
  To accomplish this task, we’ll need to add the stm8s_tim4.c/h in the project
  main.c
  stm8s_it.c
#include "stm8s.h"
main()
{
GPIO_Init(GPIOD,GPIO_PIN_0,GPIO_MODE_OUT_PP_HIGH_SLOW);
TIM4_TimeBaseInit(TIM4_PRESCALER_16,124);
TIM4_ITConfig(TIM4_IT_UPDATE,ENABLE );
TIM4_Cmd(ENABLE);
enableInterrupts();
while (1) {
}
}
INTERRUPT_HANDLER(TIM4_UPD_OVF_IRQHandler, 23){
static u16 Counter = 0;
TIM4_ClearITPendingBit(TIM4_IT_UPDATE);
if(Counter >= 999){
GPIO_WriteReverse(GPIOD,GPIO_PIN_0);
Counter = 0;
}
else{
Counter++;
}
}

## Slide 73: Hands On
GPIO
ADC
TIM4
UART

## Slide 74: Library

## Slide 75: Library

## Slide 76: Library

## Slide 77: UART
Let’s Configure UART to enter in loopback mode and receive what we send! Receive using interrupt

## Slide 78: UART
#include "stm8s.h"
main()
{
GPIO_Init(GPIOD,GPIO_PIN_0,GPIO_MODE_OUT_PP_HIGH_SLOW);
GPIO_Init(GPIOD,GPIO_PIN_5,GPIO_MODE_OUT_PP_LOW_FAST);
GPIO_Init(GPIOD,GPIO_PIN_6,GPIO_MODE_IN_PU_NO_IT);
UART1_Init(9600, UART1_WORDLENGTH_8D,
UART1_STOPBITS_1, UART1_PARITY_NO,
UART1_SYNCMODE_CLOCK_DISABLE, UART1_MODE_TXRX_ENABLE);
UART1_ITConfig(UART1_IT_RXNE_OR,ENABLE);
UART1_Cmd(ENABLE);
enableInterrupts();
UART1_SendData8('a');
while(UART1_GetFlagStatus(UART1_IT_TC) == RESET);
Delay(1000);
UART1_SendData8('b');
while(UART1_GetFlagStatus(UART1_IT_TC) == RESET);
Delay(1000);
UART1_SendData8('c');
while(UART1_GetFlagStatus(UART1_IT_TC) == RESET);
Delay(1000);
while (1) {
}
}

## Slide 79: UART
INTERRUPT_HANDLER(UART1_RX_IRQHandler, 18)
{
static char i = 0;
recebe[i] = UART1_ReceiveData8();
UART1_ClearITPendingBit(UART1_IT_RXNE);
i++;
}

## Slide 80: Thank You